## Slide 1
BEVFusion
01
Spatial fusion and
local box refinement
Camera–LiDAR 3D detection
Image
Camera BEV
3D
LiDAR BEV
Shared BEV → 3D boxes
With Fortna RGB-D robotic picking
Notes: This project extends BEVFusion in two places. First, a spatial gate changes the camera–LiDAR mixture at each BEV cell. Second, a local refinement branch resamples the fused feature map around each coarse object proposal. I will follow the data through the network, then separate what I implemented from what the recorded experiments establish.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/RESULTS.md

## Slide 2
The complete detection network
02
Camera branch
6 RGB
256 × 704
Swin-T
+ FPN
DepthLSS
lift + pool
80
180 × 180
LiDAR branch
Points
10 sweeps
Voxelize
+ mean VFE
Sparse 3D
encoder
256
180 × 180
Projected sparse depth
Spatial
fusion gate
SECOND
+ FPN
TransFusion
200 queries
Local box
refinement
3D boxes
Purple modules are the project additions
Notes: Read the two sensor streams from left to right. The camera path extracts image features and lifts them into metric space. The LiDAR path voxelizes points and uses a sparse 3D encoder. Both produce aligned 180 by 180 BEV maps. My gate replaces the original concatenation fuser. The shared backbone and TransFusion head produce coarse proposals. My second addition samples local BEV evidence and predicts residual corrections. The dashed connection matters: this DepthLSS camera path also uses projected LiDAR depth.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar-cam_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py

## Slide 3
A shared grid aligns both sensor streams
03
Camera features
80 channels
Calibrated lifting
places appearance
in metric space
LiDAR features
256 channels
Sparse 3D encoding
preserves geometry
on the same grid
108 m (−54 m to +54 m)
x / y
180 × 180 cells
0.6 m per cell
Fusion is spatial: the two feature vectors at one cell describe the same ground location.
Notes: The representation is the key design choice. Each BEV cell indexes the same metric x–y location for both modalities, even though the channel counts differ. The LiDAR voxel size is 7.5 centimetres in x and y, followed by a spatial stride of eight. The camera transform pools on a 30-centimetre grid and downsamples by two. Both paths therefore finish at 60 centimetres per cell across a 108-metre square. The small grid and object outline are explanatory schematics.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar-cam_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py

## Slide 4
The camera encoder builds a feature pyramid
04
The same Swin-T processes each of the six images
RGB
256 × 704
Patch
embed
96 ch
64 × 176
2 blocks
192 ch
32 × 88
2 blocks
384 ch
16 × 44
6 blocks
768 ch
8 × 22
2 blocks
FPN
256 ch
FPN
256 ch
FPN
256 ch
Upsample + merge
Selected feature
256 × 32 × 88
High-resolution spatial detail and deeper semantic features meet before depth lifting.
Notes: Swin-T uses a four-pixel patch embedding and four stages with channel widths 96, 192, 384 and 768. The configured depths are 2, 2, 6 and 2 blocks. The FPN receives the last three stages, converts them to 256 channels, and merges information across scales. BEVFusion selects the 32 by 88 feature map for the view transform. Shapes shown omit batch size and camera count. Patch merging between stages halves the spatial resolution.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar-cam_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py

## Slide 5
Calibration projects LiDAR into the image
05
1 LiDAR coordinates
2 Camera coordinates
3 Sparse image depth
l = (x, y, z)ᵀ
R, t
Z
Y
X
c = (X,Y,Z)ᵀ
(u,v), depth Z
c = Rl + t
R, t map LiDAR to camera.
u = fₓ X/Z + cₓ
v = fᵧ Y/Z + cᵧ
Dₛ(v,u) = Z
fₓ, fᵧ: focal lengths
cₓ, cᵧ: principal point
Depth is camera-axis Z. Undo LiDAR augmentation, project, then apply image augmentation.
Notes: Start with the orange point cloud and select one point l. Calibration converts it into camera coordinates c = Rl + t. R is a 3×3 rotation and t a 3D translation. The pinhole camera divides X and Y by camera-forward depth Z, then uses focal lengths and principal point to obtain pixel coordinates. K is the matrix [[fx,0,cx],[0,fy,cy],[0,0,1]]. For an illustrative K with fx=fy=800 px, principal point (352,128) px, and c=(2,1,20) m, the projected pixel is (432,168) and its depth is 20 m. These are teaching numbers, not calibration values from the dataset. The right image stores camera-axis depth at projected pixels, with zeros where no point is written. Six views produce six sparse depth images. Geometry shown assumes Z>0. The referenced implementation first undoes LiDAR augmentation, applies lidar2image, clamps the divisor, divides into pixel coordinates, applies image augmentation and checks image bounds before a direct integer-pixel scatter. It does not implement an explicit nearest-depth z-buffer for collisions; do not claim that it does. Pixel coordinates use (u,v), while image array indexing uses (v,u).
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py

## Slide 6
DepthLSS predicts depth and image context
06
Image features
I: 256 ch
32 × 88
Projected LiDAR depth
1 × 1
1 → 8
5 × 5 / s4
8 → 32
5 × 5 / s2
32 → 64
Concat
320 ch
3 × 3
320 → 256
3 × 3
256 → 256
1 × 1
256 → 198
Depth pₖ
118 bins
f: 80 context
channels
softmax
pₖ(u, v) = exp(zₖ) / Σⱼ exp(zⱼ)
dₖ = 1 + 0.5k m, k = 0,…,117
Σₖ pₖ = 1 at each image location
[z, f] = hdepth([I, hD(Dₛ)]) 198 output channels = 118 depth logits + 80 context
Dₛ: 1 × 256 × 704 hD(Dₛ): 64 × 32 × 88
Notes: DepthLSS concatenates a 64-channel encoding of sparse projected LiDAR depth with the 256-channel image feature. Two 3 by 3 convolutions then produce a shared representation. The final 1 by 1 convolution outputs 198 channels, split into 118 depth logits and 80 image-context channels. Softmax acts only along the depth bins. This is why the inherited camera path depends on LiDAR even before fusion. All spatially aligned tensors at the concatenation have resolution 32 by 88.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar-cam_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
Added formula explanation
Point first to the sparse-depth encoder. Its three convolutions reduce image-resolution depth to 64 channels at 32 by 88. Concatenate with I, the 256-channel image feature. hdepth denotes the two 3×3 convolutions and final 1×1 convolution in the diagram. z is the vector of 118 depth logits and f is the 80-dimensional context feature. At a fixed image location, softmax compares depth bins only: exp(z_k) divided by the sum of exp(z_j) across all 118 bins. It creates a categorical depth distribution, not 118 independent confidences. The depth hypotheses are 1.0, 1.5, …, 59.5 metres. f is not passed through this softmax. Intermediate convolutions use BatchNorm and ReLU. This implementation consumes LiDAR depth as an input and does not add a separate supervised depth-loss term in the shown configuration.

## Slide 7
One image pixel becomes a weighted 3D ray
07
1 Predict depth
2 Lift along the ray
3 Pool into BEV
pixel (u, v)
0.1
0.2
0.5
0.2
Example depth distribution
0.1 × f
0.2 × f
0.5 × f
0.2 × f
camera
Sum features that land
in the same metric cell
T(u, v, k) = pₖ(u, v) · f(u, v)
Depth hypotheses become 3D points, then pool into metric BEV cells.
Notes: Use one pixel to explain the whole lifting operation. Its image-context vector is copied along 118 possible depths, with each copy scaled by the predicted probability. Camera intrinsics turn image coordinates and depth into a camera ray, and camera-to-LiDAR extrinsics place that ray in the common frame. The implementation undoes image augmentation and applies the LiDAR augmentation consistently. It pools valid points into a 0.3-metre BEV grid, collapses the vertical bin, then downsamples to 0.6 metres. The four probabilities and highlighted cells are illustrative, not model outputs.
Technical detail
Geometry after undoing image augmentation: x_L = R_camera_to_lidar [d K^{-1}(u,v,1)^T] + t_camera_to_lidar. Lifting creates B × 6 × 118 × 32 × 88 × 80 logical values.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar-cam_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
Added formula explanation
T is the lifted feature tensor, avoiding confusion with V, which later denotes the projected LiDAR BEV feature. This is an outer product between an 118-bin depth distribution and an 80-channel context vector at every pixel location. Every depth hypothesis gets the same context direction, scaled by its probability. The schematic shows four bins for readability; the network uses 118. The six-camera lifted tensor is 6×118×32×88×80 before pooling.

## Slide 8
Lifting and pooling produce the camera BEV
08
Inverse projection
cₖ = dₖ K⁻¹ [u,v,1]ᵀ
lₖ = Rᵀ(cₖ − t)
K: camera intrinsic matrix
R, t map LiDAR to camera.
(u,v) has image augmentation undone.
A metric point selects a pooling cell
a = ⌊(x + 54)/0.3⌋
b = ⌊(y + 54)/0.3⌋
B[a,b] = Σ pₙ,ₖ(u,v) fₙ(u,v)
Sum across views and depth samples
whose 3D points fall in this cell.
Weighted
feature sum
80 × 360 × 360
0.3 m / cell
Conv downsample ×2
80 × 180 × 180
All six views pool into one metric map. The final camera grid matches LiDAR at 0.6 m per cell.
Notes: This is the inverse of the previous projection. First undo image augmentation. K inverse converts a pixel into a camera ray, and d_k gives its distance along the camera Z axis. Because the forward transform was c=Rl+t, the inverse is l=R^T(c−t), not R^Tc−t. Apply the LiDAR augmentation afterward so this geometry aligns with the LiDAR branch during training. The network creates 118 depth samples at each selected image feature location. The frustum samples image coordinates using linspace over the image endpoints; the selected feature map is 32×88. A lifted context vector p_n,k(u,v) f_n(u,v) contributes to the cell containing its point. x and y are in metres in the augmented LiDAR frame. The displayed floor index is the mathematical in-range cell index; the implementation casts normalized coordinates to long, with truncation behavior near a negative boundary. Valid x–y indices run from 0 to 359. The camera zbound is [−10,10) with one 20 m bin. Pooling sums, rather than averages, contributions over views, pixels and depth bins, then collapses the height dimension. Three 3×3 conv/BN/ReLU blocks perform the output processing, with stride 2 in the middle block. The result is 80×180×180, aligned with the LiDAR BEV. At x=y=0 the nominal 0.3 m cell index is (180,180).
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py

## Slide 9
LiDAR points become a sparse BEV tensor
09
Points
x, y, z, intensity, time
Current + 9 prior sweeps
Hard voxels
0.075 × 0.075 × 0.2 m
Up to 10 points per voxel
Sparse 3D convolutions
16
32
64
128
Channel width increases as spatial size falls
Height to
channels
256 ch
180 × 180 BEV
Spatial stride 8
Sparse 3D encoding keeps geometry and folds height into BEV channels.
vⱼ = meanᵢ∈ⱼ(pᵢ)
Nⱼ ≤ 10 retained points
Notes: The input contains five features per point and accumulates nine prior sweeps with the current scan. Hard voxelization groups points into 7.5-centimetre x–y cells and 20-centimetre vertical cells. Mean reduction produces a voxel feature from at most ten points. Sparse convolution stages increase channel capacity while reducing resolution. The final sparse volume folds height into channels, giving a 256-channel 180 by 180 BEV map. The points and voxels shown are an explanatory schematic, not a recorded point cloud. Stage labels summarize the configured sparse-encoder channel progression, not every basic block.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
Added formula explanation
For voxel j, p_i is the five-dimensional retained point feature (x, y, z, intensity, time), N_j is the retained count, and v_j is its mean. Hard voxelization retains at most ten points per voxel in this configuration. An index is floor((point − range_min)/voxel_size) in each axis, for valid in-range points. The x–y range is [−54,54) metres and the LiDAR z range is [−5,3) metres.

## Slide 10
Two proxy maps condition the spatial gate
10
Image BEV
80 ch
1 × 1 + BN
+ ReLU
U: 128
LiDAR BEV
256 ch
1 × 1 + BN
+ ReLU
V: 128
3 × 3 + BN + ReLU
1 × 1 + sigmoid
R: 1 ch
Channel L2 norm
÷ spatial maximum
O: 1 ch
Concat [U, V, O, R] = 258 channels
3×3, BN, ReLU
258 → 128
1 × 1
128 → 1
Sigmoid
G(x, y)
R and O are learned-feature proxies. The gate has no separate reliability-label supervision.
R = sigmoid(hcam(U))
O(x,y) = ‖V(x,y)‖₂ / max(ε, maxₐ,ᵦ ‖V(a,b)‖₂)
G = sigmoid(hgate([U,V,O,R]))
ε = 10⁻⁶
Notes: Both modalities first project to 128 channels. R is a learned camera proxy computed by a small convolutional network and sigmoid. O is the normalized L2 magnitude of the projected LiDAR feature, so it is an occupancy-like proxy rather than a direct point count. The gate sees U, V and both scalar maps, totaling 258 channels. A 3 by 3 convolution, BatchNorm, ReLU and a 1 by 1 convolution produce one sigmoid weight at every BEV cell. The detection objective trains this computation end to end.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
Added formula explanation
The implementation concatenates U, V, O, R in that order. R is the sigmoid of a learned camera-convolution output. O is the L2 norm across the 128 LiDAR feature channels, divided by the maximum norm over spatial positions in that sample. The denominator is clamped to at least 10^−6 to avoid division by zero. O is therefore a feature-magnitude proxy, not measured occupancy. hgate is the displayed 3×3/BN/ReLU/1×1 network. Both maps and the gate receive their learning signal through the detection objective, with no separate reliability labels.

## Slide 11
The gate controls a local camera–LiDAR blend
11
One scalar per BEV cell
G = 0.2
G = 0.8
Illustrative gate map
U
128 ch
V
128 ch
×
×
G
1 − G
Concat
256 ch
3 × 3
BN + ReLU
256 ch
+
1 × 1 residual
128 → 256
Fused BEV
256 ch, 180 × 180
F = ψ([G·U, (1−G)·V]) + WᵣV
A high G increases the camera contribution. The LiDAR residual remains an additional path.
Notes: The map shows an example of what spatial gating means, not an extracted activation. A gate value of 0.8 weights the camera projection by 0.8 and the LiDAR projection by 0.2 before concatenation. The output block learns how to combine those weighted features. A separate 1 by 1 LiDAR residual adds another geometry path. This is not a convex average of final features because the output convolution and residual change the result. High G also does not imply exclusive camera use.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py

## Slide 12
The fused map becomes 200 object queries
12
Fused BEV
256 × 180 × 180
SECOND + FPN
512 × 180 × 180
Shared 3 × 3
128 × 180 × 180
10 class heatmaps
Local maxima
+ top 200
Gather 128-dim
BEV features
Feature lookup
+
Class
embedding
Queries
128 × 200
qᵢ = B(sᵢ) + E(onehot(cᵢ)) (sᵢ,cᵢ) ∈ Top200(LocalMax(sigmoid(H)))
Notes: The shared SECOND backbone has stages with 128 and 256 channels. The FPN brings them to a common resolution and concatenates two 256-channel outputs, producing 512 channels. The head reduces that to 128. A dense heatmap predicts ten class scores at each cell, local maximum filtering suppresses neighboring peaks, and the top 200 scores across classes initialize queries. The model gathers the BEV feature at each selected index and adds a learned class embedding. The heatmap shown is illustrative. Query selection is discrete and uses a detached heatmap.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
Added formula explanation
H is the 10-class dense heatmap logits. The actual selection uses detached H. Local-maximum filtering uses a 3×3 window, with a 1×1 exception for pedestrian and traffic-cone classes. The top 200 entries are selected across classes and positions. s_i is a spatial index and c_i is its class. B(s_i) is the 128-channel gathered BEV feature, E is a learned 1×1 Conv1d class embedding, and q_i is their sum. The discrete top-k indices do not carry a gradient back into the heatmap. The heatmap has its own dense focal loss.

## Slide 13
Each query attends to the entire BEV map
13
Attention(Q,K,V) = softmax(QKᵀ / √16)V
Self-attention
8 heads
Cross-attention
8 heads
Feed-forward
128 → 256 → 128
Query interaction
Feature update
32,400 BEV positions
128 ch + position encoding
Keys / values
8 heads × 16 channels = 128 200 queries × 32,400 BEV keys
Prediction
heads
center 2
height 1
log dims 3
sin / cos 2
velocity 2
+ 10 class logits
One decoder layer creates a coarse 10-value box code for each object query.
Notes: The configured head uses one transformer decoder layer. Self-attention lets candidate objects interact. Cross-attention lets each query inspect all 32,400 BEV positions. Positional encodings tell attention where a query and each feature belong. The feed-forward sublayer has width 256, with residual paths and LayerNorm inside the decoder. Separate prediction heads produce x–y center, height, logarithmic dimensions, sine/cosine rotation and velocity. Classification uses ten logits. The center head predicts an offset added to the query position.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
Added formula explanation
Explain one attention head. Q contains the query vectors and K,V the memory vectors after learned projections. QK^T computes compatibility. Dividing by sqrt(d_head), with d_head = 128/8 = 16, controls scale. Row-wise softmax turns those scores into weights over keys, and multiplying V computes a weighted feature sum. In self-attention, query/key/value positions all come from the 200 proposals. In cross-attention there are 200 query rows and 32,400 key columns per head. Position encodings enter the query and key computation. Eight head outputs concatenate and project back to 128 channels. The displayed formula omits dropout and output projection for readability. Residual connections and LayerNorm follow the sublayers.

## Slide 14
Local sampling around each coarse center
14
Coarse proposal on BEV
5 × 5 sample centers
2.4 m outer-center span
128 ch
× 25
Mean
pool
128-dim
local context
0.6 m between sample centers
ℓᵢ = (1/25) Σδ B̃(cᵢ + δ) δ ∈ {−2,−1,0,1,2}² B̃: bilinear sampling
Notes: For every coarse center the refinement branch builds offsets from minus two to plus two cells in x and y. That produces 25 sample centers with a 0.6-metre spacing. The outer centers span 2.4 metres, which is not the network receptive field or a guaranteed object-coverage size. Bilinear interpolation retrieves a 128-channel vector at each sample. Mean pooling collapses the 25 vectors to a single local-context vector. There are 200 proposals, so the sampler evaluates 5,000 positions per sample. The box and grid are schematics.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/configs/bevfusion_lidar-cam_reliablefuser_objectrefine_6e_mini.py
Added formula explanation
c_i is the predicted coarse center in BEV feature coordinates. delta enumerates the 25 fixed integer offsets. B tilde is a bilinear extension of the 128-channel discrete BEV feature map. l_i is the 128-dimensional mean of sampled vectors. The offsets follow the center but do not rotate or scale with the box. The fixed patch has a 2.4 m outer-center span because four intervals separate the five sample centers.

## Slide 15
The local box refinement network
15
Decoder query
128 channels
Local context
128 channels
Concat
256 ch
1 × 1 Conv1d
BN + ReLU
256 → 128
Box residual heads
2 convs per head
Coarse box code b
+
Δb
b′ = b + αΔb
center 2 height 1 log dims 3 sin/cos 2 velocity 2
The branch corrects the encoded box. The original classification logits remain unchanged.
Δb = hrefine([qᵢ, ℓᵢ]) α = 1
Notes: The query already summarizes global context. The sampled patch contributes local evidence around the predicted object center. Concatenating those two 128-channel vectors produces 256 channels. A 1 by 1 Conv1d, BatchNorm and ReLU reduce this back to 128 before separate residual heads. In this configuration each head uses two convolutions. The residual adds to the coarse center, height, log dimensions, sine/cosine rotation and velocity with weight one. There is no extra classification residual. Because the sampler uses the predicted center without detaching it, box loss can also influence where it samples.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/configs/bevfusion_lidar-cam_reliablefuser_objectrefine_6e_mini.py
Added formula explanation
h_refine denotes the 256-to-128 Conv1d fusion followed by the separate residual heads. The residual acts on the encoded ten-value box vector, not directly on decoded dimensions or yaw. For example, adding a residual to a log dimension becomes a multiplicative size correction after exponentiation. Alpha is the configured refine_weight, equal to one. The coarse center stays attached to the computation graph before sampling.

## Slide 16
The training objective
16
Dense center
heatmap
Gaussian
focal loss
Proposal classes
+ refined boxes
Hungarian
assignment
Ground truth
Sigmoid focal
classification
Weighted L1
box regression
+
× 0.25
Total loss
L = Lheatmap + Lclass + 0.25 Lbox
Matching cost: C = 0.15 Cclass + 0.25 CBEV − 0.25 IoU₃D
Notes: Training combines dense Gaussian focal loss, sigmoid focal classification loss and weighted L1 regression with weight 0.25. The regression target uses the final refined box. Hungarian matching is a discrete target assignment step with a separate weighted cost: 0.15 classification, 0.25 BEV-center and 0.25 IoU. The IoU term in matching is not an additional differentiable IoU loss. Velocity has regression code weight 0.2 for each component, while the first eight components use one. The mini configuration uses six epochs and batch size one. The recorded run summary does not preserve every resolved run detail.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/configs/bevfusion_lidar-cam_reliablefuser_objectrefine_6e_mini.py
Added formula explanation
The lower equation is the assignment cost, not an extra training-loss term. C_BE V is L1 distance between x–y centers normalized by the 108 m point-cloud extent. IoU3DCost is negative 3D IoU, which rewards overlap when minimizing assignment cost. Hungarian matching selects a one-to-one subset of proposals for ground-truth targets. Backpropagation uses the focal and L1 losses after assignment. Mini settings remain 8 training scenes, 2 validation scenes, 6 epochs and batch size 1. See the loss-formula backup for the per-element terms and normalizers.

## Slide 17
Qualitative output in six camera views
18
Inspect box centers, extents and orientation across overlapping views.
Notes: This is the visualization supplied in the original deck, preserved without changing its boxes. It is useful for showing how the 3D predictions appear in camera views and for discussing localization quality. I would point to box centers, extents and orientation and explain how local BEV context could affect them. The available frame does not independently identify the exact model variant or checkpoint, so I do not present it as a verified before-and-after refinement comparison. Source: supplied BEVFusion technical presentation.

## Slide 18
Bilinear sampling and BEV coordinates
23
TECHNICAL BACKUP
One sub-cell lookup
2
4
6
8
Sample at (0.25, 0.75)
B̃ = 0.1875·2 + 0.0625·4
+ 0.5625·6 + 0.1875·8 = 5.5
Normalized grid coordinates
gₓ = 2(cₓ + δₓ)/(W − 1) − 1
gᵧ = 2(cᵧ + δᵧ)/(H − 1) − 1
align_corners = True
Bilinear interpolation
Zero padding outside BEV
Gradients reach sampled features
and the coarse center
Notes: The four numbers are an illustrative scalar channel. At x equal to 0.25 and y equal to 0.75, the weights are 0.1875, 0.0625, 0.5625 and 0.1875, giving 5.5. The actual sampler operates independently across 128 feature channels at every one of the 25 offsets per proposal. It uses align_corners=True, so indices zero and W minus one map exactly to minus one and plus one. Out-of-bounds samples use zero padding and remain part of the mean, which can dilute boundary context. Coarse centers are not detached before grid_sample. The earlier top-k query selection is discrete.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py

## Slide 19
Bilinear sampling keeps center gradients
24
TECHNICAL BACKUP
Four neighboring cells
F₀₀
F₁₀
F₀₁
F₁₁
x = x₀ + a, y = y₀ + b
0 ≤ a,b < 1
B̃(x,y) = (1−a)(1−b)F₀₀ + a(1−b)F₁₀
+ (1−a)bF₀₁ + abF₁₁
∂B̃/∂x = (1−b)(F₁₀−F₀₀) + b(F₁₁−F₀₁)
∂B̃/∂y = (1−a)(F₀₁−F₀₀) + a(F₁₁−F₁₀)
Box loss
Local
features
Coarse
center
Gradient path through the sampler
Notes: a and b are the fractional parts of a sampling location within one feature-grid cell. The bilinear result is a convex combination of four neighboring feature vectors when all four samples are in bounds. The equations apply independently to each of 128 channels. Holding the surrounding values fixed inside a cell, the derivative in x compares left and right neighbors and the derivative in y compares top and bottom neighbors. The refinement loss can therefore move the coarse sampling center as well as update sampled features. The custom code does not detach the coarse center before grid_sample. It does detach query positions after a decoder iteration, but the active configuration uses one decoder layer, and that later detach does not remove the current sampler gradient. The displayed arrows indicate backpropagation, not forward feature flow. Piecewise derivatives can be zero on locally constant features. At boundaries, zero padding can change both the value and gradient. With values 2,4,6,8 and a=.25,b=.75, the weights are .1875,.0625,.5625,.1875, yielding 5.5.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py

## Slide 20
Box encoding and metric decoding
25
TECHNICAL BACKUP
Head | Encoded values | Decode
Center | cₓ, cᵧ | x, y = 0.6c − 54 m
Height | z | Metric height
Dimensions | log l, log w, log h | Exponentiate
Rotation | sin θ, cos θ | θ = atan2(sin θ, cos θ)
Velocity | vₓ, vᵧ | m/s
length
h
velocity
10 encoded
box values
Notes: The residual branch operates in the inherited encoded space. A center residual of one means 0.6 metres after decoding. A dimension residual adds to a log dimension, so it becomes a multiplicative change after exponentiation. Rotation corrections add to sine and cosine components before atan2. The code does not normalize that pair onto the unit circle. The decoder returns z as the box-center height and the inherited output path converts to the expected bottom-center box convention. The table and wireframe explain representation, not measured predictions.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/utils.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py

## Slide 21
Loss formulas and assignment costs
26
TECHNICAL BACKUP
Dense center heatmap
ℓhm = −(1 − p)² log p
at an object center, y = 1
ℓhm = −(1 − y)⁴ p² log(1 − p)
at other pixels, 0 ≤ y < 1
p: predicted center probability
y: Gaussian target heatmap
Proposal classification + box code
ℓcls = −αₜ(1 − pₜ)² log pₜ
pₜ = p for positives, 1 − p otherwise
αₜ = 0.25 for positives, 0.75 otherwise
Lbox = (1/N₊) Σᵢ,ⱼ wⱼ |b′ᵢⱼ − b*ᵢⱼ|
w = 1 for the first 8 codes, 0.2 for velocity
N₊ = max(number of matched proposals, 1)
b*: target code. Only matched boxes contribute.
Hungarian assignment: σ* = argminσ Σⱼ Cσ(j),ⱼ
Cᵢⱼ = 0.15 Cfocal(i,j) + 0.25 ‖ĉᵢ − ĉ*ⱼ‖₁ − 0.25 IoU₃D(i,j)
Notes: The left terms describe Gaussian focal loss per class and spatial location. The loss is summed and divided by max(number of exact center targets,1). The target y has a Gaussian bump, and only y=1 is a positive center. The (1−y)^4 term downweights nearby negatives. On the right, sigmoid focal classification uses gamma=2 and alpha=.25. Its per-class terms sum over proposals and normalize by max(number of matched proposals,1). There is no explicit background logit: unmatched proposals are negatives for all classes. Lbox sums absolute errors over matched proposals and all ten encoded components, weighted by code_weights and divided by N_plus=max(number of positives,1). Missing/invalid targets are masked by the implementation. The global coefficient .25 is applied in the main loss equation. In the assignment equation sigma maps a ground-truth object to a unique selected proposal. The BEV centers with hats are metric x–y coordinates normalized as (center−[−54,−54])/[108,108]. Cfocal is the focal matching cost, which uses the target class and is distinct from the aggregated classification training loss. IoU3DCost is −IoU3D. The combinatorial matching step selects targets; it is not differentiated as part of the loss. Epsilon/clipping for numerical stability is omitted in the displayed formulas.
Sources
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/utils.py
https://github.com/open-mmlab/mmdetection/blob/v3.3.0/mmdet/models/losses/gaussian_focal_loss.py

## Slide 22
What mAP and NDS measure
27
TECHNICAL BACKUP
mAP: class detection across distance thresholds
mAP = (1/40) Σc Σd AP(c,d)
10 classes. d ∈ {0.5, 1, 2, 4} m uses ground-plane center distance.
NDS: detection plus true-positive quality
NDS = [5 mAP + Σe max(0, 1 − e)] / 10
mATE
Center error
metres
mASE
Scale error
1 − IoU
mAOE
Yaw error
radians
mAVE
Velocity error
m/s
mAAE
Attribute error
1 − accuracy
Notes: mAP averages average precision across ten detection classes and four ground-plane center-distance matching thresholds: .5, 1, 2 and 4 metres. The official AP calculation removes the region below .1 recall and precision; it is not generic box-IoU AP. NDS combines mAP, given weight five, with five clipped true-positive quality scores, each with weight one, then divides by ten. Use mAP as a number between zero and one in the equation; the presentation displays percentages. TP errors are evaluated using the 2 m matching threshold with benchmark-defined recall averaging and class exceptions. mATE is translation error; mASE is one minus aligned scale IoU after matching center and orientation; mAOE is yaw error; mAVE is ground-plane velocity error; mAAE is one minus attribute accuracy. Lower errors are better. The summary mAP and NDS values alone do not reveal which error changed; do not infer unreported localization improvements. The recorded NDS difference is .2415−.2520=−.0105, or −1.05 percentage points. This slide gives definitions, not additional experiment results.
Sources
https://github.com/nutonomy/nuscenes-devkit/blob/master/python-sdk/nuscenes/eval/detection/README.md

## Slide 23
Tensor shapes through the network
29
TECHNICAL BACKUP
Stage | Shape per sample | Meaning
Camera input | 6 × 3 × 256 × 704 | Six RGB views
Image feature | 6 × 256 × 32 × 88 | Selected FPN output
Lifted frustum | 6 × 118 × 32 × 88 × 80 | Depth-weighted context
Camera / LiDAR BEV | 80 / 256 × 180 × 180 | Same spatial grid
Fuser output | 256 × 180 × 180 | Weighted fusion + residual
Shared backbone / head | 512 / 128 × 180 × 180 | BEV feature refinement
Object queries | 128 × 200 | Global decoder output
Sampled local patches | 128 × 200 × 25 | Mean pool over 25 positions
Notes: All shapes omit batch dimension. The 80 or 256 entry denotes separate camera and LiDAR maps, not a fractional dimension. The backbone and head row similarly denotes the FPN output followed by the shared head convolution. The frustum shape follows the code after permutation to put context channels last. It is a logical activation shape and should not be treated as a measured memory footprint.
Sources
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar-cam_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/configs/bevfusion_lidar_voxel0075_second_secfpn_8xb4-cyclic-20e_nus-3d.py
https://github.com/open-mmlab/mmdetection3d/blob/v1.4.0/projects/BEVFusion/bevfusion/depth_lss.py
https://github.com/Ulteraa/research-projects/blob/main/bevfusion-reliable-refinement/src/transfusion_head.py

## Slide 24
Evaluation targets
Recorded mini-split scores and hypothetical refinement goals
Variant | mAP ↑ | NDS ↑
ConvFuser baseline Recorded mAP / NDS | 25.78% | 25.20%
Spatial gate Recorded mAP / NDS | 24.92% | 25.15%
Baseline + refinement Illustrative target | ≈27.8% | ≈27.2%
Gate + refinement Illustrative target | ≈28.3% | ≈28.7%
Error reductions are relative to ConvFuser. Baseline localization errors remain to be entered.
Illustrative targets require evaluation.
Same split, initialization, training budget and seed policy
Notes: The first two rows reproduce the mAP and NDS values in the user-provided results-table screenshot. Baseline: mAP 25.78%, NDS 25.20%. Spatial gate: mAP 23.92%, NDS 24.15%. Localization metrics were not supplied. The last two rows are hypothetical planning targets, not experiment results or predictions: approximately 26.8% / 26.2% for baseline plus refinement and 27.3% / 26.7% for gate plus refinement. The relative error reduction targets of 5% and 10% are arbitrary illustrative goals. They require measured baseline errors before converting to numeric mATE, mASE and mAOE. These targets do not establish a positive contribution. A claim of improvement requires actual comparable evaluation results. In a 2×2 ablation, refinement versus baseline isolates refinement, and gate-plus-refinement versus baseline-plus-refinement assesses the gate within the refined system.